## Slide 1
Near Real-time Equatorial Plasma Bubble Monitoring System using GNSS at the Low Latitude Region in ASEAN
N.Tongkasem (1), L.M.M. Myint* (1), P. Supnithi(1), K. Hozumi(2), D. Lakanchanh(3), and T. Nhem(4)
School of Engineering, King Mongkut’s Institute of Technology Ladkrabang, Bangkok 10520, Thailand
National Institute of Information and Communications Technology, Koganei, Tokyo, 184-8795, JAPAN
Faculty of Engineering, National University of Laos, Lao PDR
Institute of Digital Research and Innovation, Cambodia Academy of Digital Technology, 12252, Cambodia
Introduction
Methods
Data sources and Results
Conclusions
TEC can be calculated from pseudorange, which recorded from code or carrier phase measurement.
Carrier phase pseudorange
2
(2)
(3)
(4)
(5)
1
(1)
(4)-(2)
(3)-(5)
Remove: Hardware delay, ambiguity and noise
Slant Total Electron Content
Fig. 1. The pseudorange is calculated from the delay time of the code signal correlation
Figure. The observed TEC on 10/04/2018 at KMIT station.
Ionospheric delay can be measured from TEC
Code pseudorange
Fig. 2. The pseudorange is calculated from the carrier phase tacking
recorded code pseudorange
real distance
receiver hardware delay
satellite hardware delay
noise and multipath
recorded carrier-phase pseudorange
light speed
phase
integer ambiguity
Parameters
Ionospheric delay
The amount of electron density between the satellite and the receiver, expressed in TECu (1 TECu = 10^16 electrons/m2).
According to the results, the location of the EPB can be detected by the spatial ROTI maps and their spatial-temporal variation is monitored using the keogram plots for forecasting their occurrence and movement.
In this study, we examine the spatial and temporal changes of EPBs using the spatial ROTI map, latitudinal/longitudinal keogram plots developed from the GNSS receiver network in ASEAN’s northern hemisphere low latitudes.
Develop a near real-time EPB monitoring system using Global Navigation Satellite System (GNSS) data from the receiver stations in Thailand as well as the stations in Lao and Cambodia.
Monitor EPB occurrences using daily ionospheric total electron content (TEC) and rate of TEC change index (ROTI) map and keograms,
20 GNSS stations on the Thailand region and nearby
* Presenter email: linminmin.my@kmitl.ac.th
Generate (every 15 minutes) 2D-maps (latitude and longitude) of TEC, ROTI covering the low latitude region from latitudes of N 0o from N 25o, and the longitudes from E 95o to E 110o.
Flowchart
(6)
(7)
the slant differential TEC or rate of TEC, ROT in (6) is determined by calculating the change of slant TEC between consecutive intervals time 1 minute.
The ROTI in unit of TECu/min is computed from the standard deviation of ROT
Solar 25 [space weather prediction center, NOAA]
The ascending phase of the Solar Cycle 25 are higher than the predicted sunspot number value (SSN), and higher than the peak of SSN in Solar Cycle 24.
GNSS data from GNSS stations
TEC estimation
ROTI estimation
ROTI keogram
2D ROTI map
2D TEC map
RESULTS
University of Laos (NUO2)
TEC calculation
ROTI calculation
Data source
Chart: Number Days with EPB per Month in 2022
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
Month | 1 | 4 | 15 | 13 | 3 | 1 | 1 | 2 | 16 | 28 | 13 | 3
TEC map
Preprocessing
Cycle slip correction
Low Elevation angle cut off
Cambodia Academy of Digital Technology (CADT)
King Mongkut institute of Technology Ladkrabang (KMITL)
EPB Statistics in 2022
Quiet vs Disturb
ROTI 2D map
ROTI keogram
EPB speed estimation
The direction and speed of the EPBs can be estimated using the zonal drift velocities of the EPBs shape of ROTI keogram.
Doy 282
Doy 283
Doy 282
Doy 283
ROTI latitude keogram
ROTI longitude keogram
Detect the occurrence of EPB from the generated 2D-maps using image processing of AI in future.
Acknowledgement
The ASEAN IVO (http://www.nict.go.jp/en/asean_ivo/ index.html) project, [GNSS and Ionospheric Data Products for Disaster Prevention and Aviation in Magnetic Low- Latitude Regions (Phase II)], was also involved in the production of the contents of this work and financially supported by NICT (http://www.nict.go.jp/en/index.html).
Publish on the Website: http://iono-gnss.kmitl.ac.th/